## Slide 1: THE NATIONAL INSTITUTE OF ENGINEERING MYSORE Autonomous Institue Affliated to VTU Department of Electronics and communication Engineering MINOR PROJECT PHASE -2 PRESENTATION ON “Implementation of Y86-64 processor architetecture design using hardware coding language VERILOG “
Guided by :
Dr. Narasimha kaulgud
Professor
Department Of ECE
NIE MYSORE

## Slide 2: Sequential Y86-64 Implementations
Stages in Y86-64
Fetch
Decode
Execute
Memory
WriteBack
PC update

## Slide 3: 1.Fetch
Algorithm for fetch Module
Check for Memory Error:
  If the PC value exceeds the memory boundary (e.g., 1023 in this case), set mem_error to 1 and exit.
Decode Instruction:
  Extract the icode and ifun from the instr bits.
Calculate Next PC (valP):
  Determine the next PC value based on the icode:
    For icode values 0000, 1001, 0001: valP = PC + 1
    For icode values 0010, 0110, 1010, 1011: valP = PC + 2
    For icode values 0011, 0100, 0101: valP = PC + 10
    For icode values 0111, 1000: valP = PC + 9
Extract Operands (if applicable):
  Based on the icode:
    Extract rA and rB from the instr bits if applicable.
    Extract valC from the instr bits if applicable.
Set instr_error:
  If the icode value is not recognized, set instr_error to 1.

## Slide 4: 2.Decode
Algorithm for Decode Stage
Initialize:
  Set valA and valB to 0.
Decode Instruction:
  Check the value of icode:
    If icode is 6 (opq):
      Set valA to the value of register rA.
      Set valB to the value of register rB.
    If icode is 2 (cmovxx):
      Set valA to the value of register rA.
      Set valB to 0.
    If icode is 4 (rmmov):
      Set valA to the value of register rA.
      Set valB to the value of register rB.
    If icode is 5 (mrmov):
      Set valB to the value of register rB.
    If icode is 10 (push A):
      Set valA to the value of register rA.
      Set valB to the value of register 4 (assuming %rsp is in register 4).

## Slide 5
    If icode is 11 (pop B):
      Set valA to the value of register 4 (assuming %rsp is in register 4).
      Set valB to the value of register 4 (assuming %rsp is in register 4).
    If icode is 8 (call):
      Set valB to the value of register 4 (assuming %rsp is in register 4).
    If icode is 9 (ret):
      Set valA to the value of register 4 (assuming %rsp is in register 4).
      Set valB to the value of register 4 (assuming %rsp is in register 4).

## Slide 6: 3.Execute
Algorithm for Execute Stage
Calculate Condition Flag (cnd):
  If icode is 2 (cmovxx) or 7 (jxx):
    Determine the cnd value based on the ifun and the current flags (zf, sf, of):
      ifun = 0000 (uc): cnd = 1 (unconditional)
      ifun = 0001 (le): cnd = (sf ^ of) | zf
      ifun = 0010 (l): cnd = of ^ sf
      ifun = 0011 (e): cnd = zf
      ifun = 0100 (ne): cnd = ~zf
      ifun = 0101 (ge): cnd = ~(sf ^ of)
      ifun = 0110 (g): cnd = ~(sf ^ of) & ~zf
  Otherwise, set cnd to 0.
Perform ALU Operations:
  Based on the icode:
    If icode is 2 (cmovxx):
      Perform the ALU operation for cmovxx (e.g., pass valA to valE_cmov).
    If icode is 3 (irmov), 4 (rmmov), or 5 (mrmov):
      Perform the ALU operation for memory moves (e.g., pass valC to valE_cb).

## Slide 7
    If icode is 6 (opq):
      Perform the ALU operation specified by ifun on valA and valB and store the result in valE_op.
      Calculate cf_out based on the result of the ALU operation:
        Set cf_out[0] (zero flag) to 1 if valE_op is 0, otherwise 0.
        Set cf_out[1] (sign flag) to the value of the most significant bit of valE_op.
        Set cf_out[2] (overflow flag) to the value of overflow_use from the ALU operation.
    If icode is 8 (call) or 10 (push A):
      Perform the ALU operation for stack decrement (e.g., subtract 8 from valB and store the result in valE_sd).
    If icode is 9 (ret) or 11 (pop B):
      Perform the ALU operation for stack increment (e.g., add 8 to valB and store the result in valE_si).
Select Output (valE):
  Based on the icode:
    If icode is 2 (cmovxx): valE = valE_cmov
    If icode is 3 (irmov), 4 (rmmov), or 5 (mrmov): valE = valE_cb
    If icode is 6 (opq): valE = valE_op
    If icode is 8 (call) or 10 (push A): valE = valE_sd
    If icode is 9 (ret) or 11 (pop B): valE = valE_si
    Otherwise, valE = 0

## Slide 8: 4.Memory
Algorithm for Memory Stage
Data Memory Access:
  Based on the icode:
    If icode is 4 (rmmov) or 10 (pushq):
      Store the value of valA in the memory location specified by valE.
    If icode is 5 (mrmov):
      Load the value from the memory location specified by valE into valM.
    If icode is 11 (popq):
      Load the value from the memory location specified by valA into valM.
    If icode is 8 (call):
      Store the value of valP (next instruction address) in the memory location specified by valE.
    If icode is 9 (ret):
      Load the value from the memory location specified by valA into valM.
(Optional) Data Memory Initialization:
  For debugging or testing purposes, you can initialize specific memory locations with predefined values. The example code initializes location valA with 200 and location valE with 100.

## Slide 9
5. WRITE BACK
Algorithm for write_back Stage
Update Register File:
  On the negative edge of the clock:
    Load the input register values (reg_in0 to reg_in14) into the internal register file (reg_file).
    Based on the icode:
      If icode is 6 (opq), 2 (cmovxx), or 3 (irmov):
        Write the value of valE to the register specified by rB.
      If icode is 11 (popq):
        Write the value of valE to register 4 (%rsp).
        Write the value of valM to the register specified by rA.
      If icode is 8 (call), 9 (ret), or 10 (pushq):
        Write the value of valE to register 4 (%rsp).
      If icode is 5 (mrmov):
        Write the value of valM to the register specified by rA.
Output Register Values:
  Assign the values from the internal register file (reg_file) to the output ports (reg_out0 to reg_out14).

## Slide 10: 6.PC_Upadte
Algorithm for Pc update Module
On the Positive Edge of the Clock:
  Based on the icode:
    If icode is 0000: Set pcnxt to 0.
    If icode is 0111 (jxx):
      If cnd is 1 (condition is true): Set pcnxt to valC (jump target).
      Otherwise, set pcnxt to valP (next instruction address).
    If icode is 1000 (call): Set pcnxt to valC (call target).
    If icode is 1001 (ret): Set pcnxt to valM (return address).
    For all other icode values: Set pcnxt to valP (next instruction address).

## Slide 11: Testbench Instructions